## Slide 1: 임베디드시스템설계및실험
DMA (Direct Memory Access)

## Slide 2
to provide high-speed data transfer between peripherals and memory
data can be quickly moved by DMA without any CPU actions
Direct Memory Access
DMA introduction

## Slide 3
12 independently configurable channels
  each of the 12 channels is connected to dedicated hardware DMA requests
  priorities between requests from channels of one DMA are software programmable
independent source and destination transfer size (byte, half word, word)
support for circular buffer management
3 event flags
  DMA Half Transfer, DMA Transfer Complete and DMA Transfer Error
memory-to-memory transfer
peripheral-to-memory, memory-to-peripheral and peripheral-to-peripheral
programmable number of data to be transferred: up to 65536
Direct Memory Access
DMA main features

## Slide 4
DMA1 controller
  the 7 requests from the peripherals (TIMx[1,2,3,4], ADC1, SPI1, SPI1/I2S2, I2Cx[1,2,] and USARTx[1,2,3]) are simply logically ORed before entering the DMA1
  only one request must be enabled at a time
Direct Memory Access
DMA request mapping

## Slide 5
DMA2 controller
  the 5 requests from the peripherals (TIMx[5,6,7,8], ADC3, SPI/I2S3, USART4, DAC_Channel[1,2] and SDIO) are simply logically ORed before entering the DMA2
  only one request must be enabled at a time
Direct Memory Access
DMA request mapping

## Slide 6
see stm32f10x_dma.c and stm32f10x_dma.h
DO NOT HAVE TO use interrupt
수업 발표 내용
  DMA 정의, 동작 방법, 효과
  보드에서의 DMA 동작 및 사용 방법
  실험 방법
  조사하여 발표
Direct Memory Access